## Slide 1: HNDIT2401 Computer Architecture
Week 3: Internal Components of CPU and its functions

## Slide 2: CPU
The central processing unit (CPU) is responsible for fetching program instructions, decoding each instruction that is fetched, and performing the indicated sequence of operations on the correct data.
The performance of a machine is directly affected by the design of the data path and the control unit.

## Slide 3: CPU Function
CPU must:
  Fetch instructions
  Interpret/decode instructions
  Fetch data
  Process data
  Write data
Notes: 22

## Slide 4: CPU With Systems Bus

## Slide 5: CPU Basics and Organization
Registars
The ALU
The Control Unit
The Bus
Clocks

## Slide 6: The ALU
The arithmetic logic unit (ALU) carries out the logic operations (such as comparisons)and arithmetic operations (such as add or multiply) required during the program execution.
Generally an ALU has two data inputs and one data output. Operations performed in the ALU often affect bits in the status register (bits are set to indicate actions such as whether an overflow has occurred). The ALU knows which operations to performbecause it is controlled by signals from the control unit.

## Slide 7: Control Unit
The control unit is the “policeman” or “traffic manager” of the CPU. It monitors the execution of all instructions and the transfer of all information.
The control unit extracts instructions from memory, decodes these instructions, making sure data is in the right place at the right time, tells the ALU which registers to use, services interrupts, and turns on the correct circuitry in the ALU for the execution of the desired operation.
The control unit uses a program counter register to find the next instruction for execution and a status register to keep track of overflows, carries, borrows,etc

## Slide 8: Bus
The CPU communicates with the other components via a bus.
A bus is a set of wires that acts as a shared but common data path to connect multiple subsystems within the system.

## Slide 9: Clocks
Every computer contains an internal clock that regulates how quickly instructions can be executed.
The clock also synchronizes all of the components in the system.As the clock ticks, it sets the pace for everything that happens in the system,much like a metronome or a symphony conductor.
instruction performance is often measured in clock cycles—the time between clock ticks—instead of seconds
Most machine instructions require 1 or 2 clock cycles, but some can take 35 or more.

## Slide 10: CPU With Systems Bus
major components of the processor are an arithmetic and logic unit (ALU) and a control unit (CU). In addition, consisting of a set of storage locations, called registers.
The ALU does the actual computation or processing of data.
The control unit controls the movement of data and instructions into and out of the processor and controls the operation of the ALU.

## Slide 11: Registers
a Register is a hardware device that stores binary data. Registers are located on the processor so information can be accessed very quickly CPU must have some working space (temporary storage) - registers
Number and function vary between processor designs - one of the major design decisions
Top level of memory hierarchy.
D flip-flops can be used to implement registers.
Notes: 23

## Slide 12: Registers
The registers in the processor perform two roles:
User-visible registers: Enable the machine- or assembly language programmer to minimize main memory references by optimizing use of registers.
Control and status registers: Used by the control unit to control the operation of the processor and by privileged, operating system programs to control the execution of programs.

## Slide 13: MARIE ARCHI
MARIE, a Machine Architecture that is Really Intuitive and Easy, is a simplearchitecture consisting of memory (to store programs and data) and a CPU (consisting of an ALU and several registers).
It has all the functional components necessary to be a real working computer

## Slide 14: MARIE registers
AC: The accumulator, which holds data values. This is a general purpose register and holds data that the CPU needs to process. Most computers today have multiple general purpose registers.
MAR: The memory address register, which holds the memory address of the data being referenced.
MBR: The memory buffer register, which holds either the data just read from memory or the data ready to be written to memory.
PC: The program counter, which holds the address of the next instruction to be executed in the program.
IR: The instruction register, which holds the next instruction to be executed.
InREG: The input register, which holds data from the input device.
OutREG: The output register, which holds data for the output device.

## Slide 15: MARIE has the following characteristics:
Binary, two’s complement
Stored program, fixed word length
Word (but not byte) addressable
4K words of main memory (this implies 12 bits per address)
16-bit data (words have 16 bits)
16-bit instructions, 4 for the opcode and 12 for the address
A 16-bit accumulator (AC)
A 16-bit instruction register (IR)
A 16-bit memory buffer register (MBR)
A 12-bit program counter (PC)
A 12-bit memory address register (MAR)
An 8-bit input register
An 8-bit output register

## Slide 16: User Visible Registers
General Purpose
Data
Address
Condition Codes
Notes: 24

## Slide 17: General Purpose Registers (1)
May be true general purpose
May be restricted
May be used for data or addressing
Data: accumulator (AC)
Addressing: segment (cf. virtual memory), stack (points to top of stack, cf. implicit addressing)
Notes: 25

## Slide 18: General Purpose Registers (2)
Make them general purpose
  Increased flexibility and programmer options
  Increased instruction size & complexity, addressing
Make them specialized
  Smaller (faster) but more instructions
  Less flexibility, addresses implicit in opcode
Notes: 26

## Slide 19: How Many GP Registers?
Between 8 - 32
Less = more memory references
More takes up processor real estate
Notes: 27

## Slide 20: How big?
Large enough to hold full address
Large enough to hold full data types
But often possible to combine two data registers or two address registers by using more complex addressing (e.g., page and offset)
Notes: 28

## Slide 21: Condition Code Registers – Flags
Sets of individual bits, flags
  e.g., result of last operation was zero
Can be read by programs
  e.g., Jump if zero – simplifies branch taking
Can not (usually) be set by programs
Notes: 29

## Slide 22: Control & Status Registers
Program Counter (PC)
Instruction Register (IR)
Memory Address Register (MAR) – connects to address bus
Memory Buffer Register (MBR) – connects to data bus, feeds other registers
Notes: 30

## Slide 23: Program Status Word
A set of bits
Condition Codes:
  Sign (of last result)
  Zero (last result)
  Carry (multiword arithmetic)
  Equal (two latest results)
  Overflow
Interrupts enabled/disabled
Supervisor/user mode
Notes: 31

## Slide 24: Supervisor Mode
Intel ring zero
Kernel mode
Allows privileged instructions to execute
Used by operating system
Not available to user programs
Notes: 32

## Slide 25: Other Registers
May have registers pointing to:
  Process control blocks (see OS)
  Interrupt Vectors (see OS)
N.B. CPU design and operating system design are closely linked
Notes: 33

## Slide 27: MC68000 and Intel registers
Motorola:
  Largely general purpose registers – explicit addressing
  Data registers also for indexing
  A7 and A7’ for user and kernel stacks
Intel
  Largely specific purpose registers – implicit addressing
  Segment, Pointer & Index, Data/General purpose
  Pentium II – backward compatibility

## Slide 28: Indirect Cycle
Same address can refer to different arguments (by changing the content of the location the address is pointing to)
Indirect addressing requires more memory accesses to fetch operands
Can be thought of as additional instruction subcycle

## Slide 29: Instruction Cycle with Indirect

## Slide 30: Instruction Cycle State Diagram

## Slide 31: Data Flow (Instruction Fetch)
PC contains address of next instruction
Address moved to MAR
Address placed on address bus
Control unit requests memory read
Result placed on data bus, copied to MBR, then to IR
Meanwhile PC incremented by 1

## Slide 32: Data Flow (Fetch Diagram)

## Slide 33: Data Flow (Data Fetch)
IR is examined
If indirect addressing, indirect cycle is performed
  Rightmost n bits of MBR (address part of instruction) transferred to MAR
  Control unit requests memory read
  Result (address of operand) moved to MBR

## Slide 34: Data Flow (Indirect Diagram)

## Slide 35: Data Flow (Execute)
May take many forms, depends on instruction being executed
May include
  Memory read/write
  Input/Output
  Register transfers
  ALU operations

## Slide 36: Data Flow (Interrupt)
Current PC saved to allow resumption after interrupt
Contents of PC copied to MBR
Special memory location (e.g., stack pointer) loaded to MAR
MBR written to memory according to content of MAR
PC loaded with address of interrupt handling routine
Next instruction (first of interrupt handler) can be fetched

## Slide 37: Data Flow (Interrupt Diagram)

## Slide 38: Prefetch
Fetch involves accessing main memory
Execution of ALU operations do not access main memory
Can fetch next instruction during execution of current instruction, cf. assembly line
Called instruction prefetch
Notes: 36